## Slide 1: Voltron planning

## Slide 2: Timeline
1st Milestone: Present DC fabric BAF balancing and uplifted IBC Video demo at NAG/obiWAN in October
Today
(7/24)
Start
(8/2)
obiWAN
(10/25)
Milestone
(8/18)
IBC Demo
(9/15)
Milestone
(10/6)
GSX
- Define Architecture
- Create Behavioral Spec
- Build Demo Testbed
- Practice Demo
SR Summit
(9/20-21)

## Slide 3: Open Questions
Question | Jeff’s take | Direction
AWS vs. GCP vs. on-prem? | Hybrid model essential from the start; AWS for easier billing | k8s + OpenShift but support for anything vanilla, running on AWS
Separate analytics stack as part of project? | Build bindings to support 3rd-party data sources in the future, but keep analytics in-house for first phase (plus, Voltron services shouldn’t care where data are coming from) | 
Which 2 use cases to target first? | DC BAF balancer and at least part of the IBC Demo (high BW path) | IBC Demo and DC BAF balancer
Specifications for timing between data source and computations | Encode constraints as part of service spec | 
Scaling: How many devices in network? | 100 routers, 300 SIDs, 300 hosts | 100 routers, 300 SIDs, 300 hosts
Scaling: How many API requests/s? | Omar | TBD, probably scalable without extra thought
Performance: Latency bounds on API calls |  | All API calls make round trip to cloud
Footprint constraints? | Target an AIO instance for 16 cores and however much memory makes sense based on VM sizing on chosen platform. | Small/medium machines for servicing API requests, larger VMs for backend
Project organization: how many people? | TBD based on architecture | 
Project organization: sprint durations? | 3 weeks because summertime | 2 weeks suggested

## Slide 4: Open Questions
Question | Omar’s/Bruce’s/Rachael’s take | Direction
Host stack: Contiv, VPP, bare metal, etc. |  | 2 parts: generic logic to interact with Voltron, custom programmer for destination environment (k8s vs. VPP vs. Linux) – reuse Contiv plugin for now, Jeff/Bruce to investigate for more “real” solution moving forward
Data bus: Kafka? | Kafka | Kafka
Where is metric/telemetry data stored? | Neo4j as a graph DB, but need input from SW devs (Matt/Steve/Adam/Daniel) | TBD with input from Matt
Navigation of political landmines related to other products and kingdoms | Let Brook keep being Brook | 
Yet another visualization engine? | Leverage what we have with, say, pNDA | TBD, but somewhat orthogonal
Testing environment and developer visibility | What we build for ourselves is also meant for consumers | 
Software frameworks and languages to adopt? | Don’t chase the shiny new if not needed, but make sure we get Matt’s feedback | TBD with input from Matt
IPv4 vs. IPv6? | Build v6 first, v4 as the odd man out | v6 for signaling, v4 in dataplane – requires IBC uplift potentially
Team communication | Use wwwin-github.cisco.com/spa-ie for big things, Paul’s docwiki for documentation | Use wwwin-github.cisco.com/spa-ie for big things, Paul’s docwiki for documentation

## Slide 5: Runtime Flow: BAF balancing
Endpoint DB replicator container (Contiv) requests label stack to use for DB replication going from destination A to B in same DC
Voltron BAF balancer service looks at most recent utilization across the 4 fabric planes and determines least used path
Voltron responds with label associated with selected path
Container initialized so that all traffic has label appended
Go traffic go

## Slide 6: Pre-conditions: BAF balancing
API exists for endpoint to call
  The BAF balancer service has been loaded on Voltron
  The service has successfully published the API
  The service has a live responder for API queries in that path
The endpoint knows how to call the API
  It knows whom to ask
  It knows the keys of the query (src/dst IP, label vs. segment)
  It understands the reply (label or segment ID)
The endpoint knows which API to call
  Lowest-utilized-plane vs. latency vs. security, etc.
  Parameters to the API
Voltron service knows how to get the answer
  Topology information is available
  Necessary links are distinguished as planes
  Recent* bandwidth utilization is available and associated to links (and therefore planes)
Connectivity exists between endpoint and Voltron
  MTU set high enough to allow for label stack

## Slide 7: Runtime Flow: IBC High BW Video Demo
MPE requests label stack to use for video stream going from MPE to CDN destination A with minimum available bandwidth of 3Gbps
Voltron Bandwidth Broker service looks at topology and latest telemetry to determine end-to-end path with sufficient capacity
Voltron responds with label stack associated with selected path
Go traffic go with that label stack

## Slide 8: Pre-conditions: IBC High BW Video Demo
API exists for MPE to call
  The BW Broker service has been loaded on Voltron
  The service has successfully published the API
  The service has a live responder for API queries in that path
The endpoint knows how to call the API
  It knows whom to ask
  It knows the keys of the query (src/dst IP, label vs. segment, max bw parameter)
  It understands the reply (label or segment ID)
The endpoint knows which API to call
  Lowest-utilized-plane vs. latency vs. security, etc.
  Parameters to the API (max bw)
Voltron service knows how to get the answer
  Topology information is available
  Recent* bandwidth utilization is available and associated to links
Connectivity exists between endpoint and Voltron
  MTU set high enough to allow for full label stack

## Slide 9: Runtime Flow: IBC Low Latency Demo
Client send manifest request for internal cloud
Voltron Low Latency service looks at topology and latest telemetry to determine end-to-end path to meet constraints
Voltron responds with label stack
Client caches result for next request
MM receives manifest request
MM requests label stack to use for manifest going from MM to client destination A with max latency 100ms
Voltron Low Latency service looks at topology and latest telemetry to determine end-to-end path to meet constraints
Voltron responds with label stack associated with selected path
MM caches result for subsequent requests (channel changes)
IPVS applies label stack when responding with manifest
Go traffic go with that label stack

## Slide 10: Pre-conditions: IBC Low Latency Demo
API exists for Client and MM to call
  The Low Latency service has been loaded on Voltron
  The service has successfully published the API
  The service has a live responder for API queries in that path
The endpoint knows how to call the API
  It knows whom to ask
  It knows the keys of the query (src/dst IP, label vs. segment, max latency parameter)
  It understands the reply (label or segment ID)
The endpoint knows which API to call
  Lowest-utilized-plane vs. latency vs. security, etc.
  Parameters to the API (max bw)
Voltron service knows how to get the answer
  Topology information is available
  Probes to measure different paths are deployed and active
  Recent* latency measurements are available and associated to paths
Connectivity exists between {Client, MM, probes} and Voltron
  MTU set high enough to allow for full label stack

## Slide 11: Suggested work items
1) base infrastructure -diagram building (what does the thing we’re building look like) -manual deployment (proving it out by hand) -validation/service checks for basics (how do we know we have a stable foundation) -automation of deployment (how can other people do it) -automation of validation (how can other people know that the thing they built is working) -versioning (how do we track changes) -packaging (how do people get it – similar to deployment but combines versioning, too) | 2) framework -articulation of initial use cases and information flow -definition of framework templates -tooling to build/package/deploy service from definition -validation of framework and service tooling -versioning of templates and tools -incorporation into base architecture
3) tooling and support -identification/packaging of clients -testbed creation and automation -test harness for services -CI/CD strategy | 4) services (multiple) -articulation of business value -service definition (data needs, api, etc.) -information flow mapping onto architecture --gap identification -algorithm development -validation/testing -validation automation