## Slide 1: Voltron Segment Routing Architecture
Web Operation
July 2017

## Slide 2: Why Does the Host/App Never Appear in our SDN Diagrams?
We produce a lot of “SDN” material depicting controllers pushing instructions to routers and switches
A “Source” requests traffic treatment from a controller via PCEP
Controller pushes label stack instruction to Router via PCEP
Where is the Host/App in SDN architecture diagrams?
4
5
3
6
7
AS2
2
1
AS1
BGP-LS
PCEP
pkt
16007
16003
16002
SR
PCE

## Slide 3: Voltron Fundamentals
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Network Fabric
App
App
Give the Host/VM/Container/Application the ability to control its network treatment (Source Routing)
Extend Segment Routing to the Host
Big Data approach to SDN
Host
With containerized Apps

## Slide 4: SDN is a Big Data Problem
App
User
S0
L0
L8
T0
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
Metro Fabric
S0
L0
L8
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
WAN Fabric
S0
L0
L8
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
DC Fabric
ASBR
ASBR
https://www.ietf.org/id/draft-filsfils-spring-large-scale-interconnect-03.txt
Don’t think in terms of “Controller” (controllers tend to be monolithic)
Think in terms of distributed applications (your Facebook page is not assembled by a monolithic ‘web controller’)
Distributed applications = Scaled Microservice Architecture

## Slide 5: SDN is a Big Data Problem
App
User
S0
L0
L8
T0
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
Metro Fabric
S0
L0
L8
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
WAN Fabric
S0
L0
L8
L16
L64
S16
S32
S128
….
Ln
Lx
Ly
Lz
….
….
Tn
DC Fabric
ASBR
ASBR
https://www.ietf.org/id/draft-filsfils-spring-large-scale-interconnect-03.txt
Some Voltron Guiding Principles:
Prefer APIs over Protocols
Use new tools: BMP, gRPC, etc.
And BGP (always BGP)
Avoid legacy tools: SNMP, CLI, PCEP, etc. whenever possible
Avoid making config-state changes to Network/Fabric elements

## Slide 6: Network Data Collection Infrastructure
Collectors
Data Aggregation (Kafka)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Network Fabric
App
App
Host
With containerized Apps
Query
TSDB
Batch
Etc
PNDA?
Topology, Label, Prefix Data
Telemetry Data

## Slide 7: Analytics Applications
Collectors
Data Aggregation (Kafka)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Network Fabric
App
App
Host
With containerized Apps
Query
TSDB
Batch
Etc
PNDA?
WAE
GPS RTT*
$ per Gb*
* I made these two up, but they sound like cool analytics apps
Topology, Label, Prefix Data
Telemetry Data

## Slide 8: Voltron Microservices, API GW, and Host Networking
Collectors
Data Aggregation (Kafka)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Network Fabric
App
App
Host
With containerized Apps
Query
TSDB
Batch
Etc
PNDA
SR agent
SR agent
Path Selection Service
Overlay Service
Service X
API GW
Voltron
WAE
GPS RTT*
$ per Gb*
* I made these two up, but they sure sound like cool analytics apps
Topology, Label, Prefix Data
Telemetry Data

## Slide 9: Voltron Microservices, API GW, and Host Networking
Topology, Label, Prefix Data
Collectors
Telemetry Data
Data Aggregation (Kafka)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Network Fabric
App
App
Host
With containerized Apps
Query
TSDB
Batch
Etc
PNDA
SR agent
SR agent
Path Selection Service
Overlay Service
Service X
API GW
Voltron
WAE
GPS RTT*
$ per Gb*
* I made these two up, but they sure sound like cool analytics apps
XTC

## Slide 10: Initial Use Case – BAF Balancer

## Slide 11: BAF Balancer
S0
L0
L1
T0
C1
L16
L7
S16
S32
S112
….
L8
L9
L10
L15
….
….
T17
H63
C3
H0
C2
Cn
Hn
Tn
Hardware ECMP is unaware of flow-size (Elephants & Mice problem)
Can lead to traffic polarization and unbalanced network utilization
Most common bottleneck in high radix DC is egress leaf node

## Slide 12: BAF Balancer
Container / Application makes High-BW API request
Microservice maintains data cache of all DC Fabric Paths: n(n-1)/2 Leaf-Spine-Leaf tuple mesh (note: formula should be modified to reflect DC-Planes design)
Microservice fields Elephant-flow (High-BW) request, performs ToR-to-ToR lookup from base microservice, and allocates L-S-L label stack
Gap: need feedback loop informing microservice when HiBW flow is complete, so LSL tuple may be returned to ‘available’ status
Role for XTC? Do we execute changes in the network? Or do we keep a table of paths and XTC acts as load balancer?
L0
S0
L0
T0
T1
L8
S16
L9
L16
S32
L17
X
X
Avail
Elephant Flow Balancer Microservice
ToR-to-ToR: 1024 discrete LSL paths
4000 ToRs: n(n-1)/2 = 8M
8M*1024 = 8.2B possible LSL combinations
S0
L0
L1
L16
L7
S16
S32
S112
….
L1
L9
L17
L65
….
….
T0
C1
T17
H63
C3
H0
C2
Cn
Hn
Tn
REST or
RPC request
Flow Balancer Service
Collector

## Slide 13: DC Planes Reference – and Anycast SID
Anycast-SID across all or a subset of Spine nodes per plane
Example Application use case:
Reads – no steering
Writes – load balance across DC shards
20003
20002
20001
Anycast SID 20000

## Slide 14: Voltron Microservices, API GW, and Host Networking
Topology, Label, Prefix Data
Collectors
Telemetry Data
Data Aggregation (Kafka)
App
App
Host
With containerized Apps (Dockerized)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
App
Host
With containerized Apps
Query
TSDB
Batch
Etc
PNDA
SR agent
SR agent
Path Selection Service
Overlay Service
Service X
API GW
Voltron
WAE
XTC
REST API
WAN
LB Service
Is the Overlay Service simply a BGP VPNv4/6 session with RR?
GoBGP: EVPN, SR-BGP-LU, BMP

## Slide 15: SR and BGP Details

## Slide 16: Voltron SR Control Plane
BGP Prefix SID – similar to IGP Prefix SID
  Advertised via BGP Labeled-Unicast (BGP-LU)
  SRGB Values
  ECMP
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
Host
App
BGP-LU
Host
App
10.1.1.200/32
BGP-Pfx-SID 100200
10.1.1.100/32
BGP-Pfx-SID 100100
10.1.1.4/32
BGP-Pfx-SID 100004
10.1.100.0/32
BGP-Anycast-SID 110000
App, VM, or
Container

## Slide 17: Voltron BGP Config
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
Host
App
BGP-LU
Host
App
10.1.1.200
BGP-Pfx-SID 100200
10.1.1.100
BGP-Pfx-SID 100100
10.1.1.4
BGP-Pfx-SID 100004
10.1.100.0
BGP-Anycast-SID 110000
route-policy SID($SID)
set label-index $SID
end-policy
!
segment-routing global-block 100000 164999
!
router bgp 3
bgp router-id 1.1.1.3
address-family ipv4 unicast
network 10.1.1.200/32 route-policy SID(200)
allocate-label all

## Slide 18: Voltron SR Dataplane
Base connectivity example; ie, no host control yet…
BGP Prefix SID Dataplane
  Ingress pushes SID-value (label) for destination
  LSR nodes perform label swaps
  PHP
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
Host
App
Host
App
payload
IP
100200
payload
IP
ToR100
payload
IP
100200
LeafN
payload
IP
100200
SpineN
payload
IP
LeafN
payload
IP
ToR200

## Slide 19: Voltron SR Dataplane
Egress Engineering, aka EPE SID – similar to IGP adj SID
  Non-SRGB, Local to the router
  Can be used to steer traffic via specific interface(s)
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
Host
App
Host
App
EPE SIDs
Gi0/0/0/0 24008
Gi0/0/0/1 24009
Gi0/0/0/2 24010
Gi0/0/0/3 24011
EPE SIDs
Gi0/0/0/0 24011
Gi0/0/0/1 24010
Gi0/0/0/2 24009
Gi0/0/0/3 24008
EPE SIDs
Gi0/0/0/0 24000
Gi0/0/0/1 24001
Gi0/0/0/2 24002
Gi0/0/0/3 24003
payload
IP
100200
24008
Host
payload
IP
Leaf6 to Tor
24008
payload
IP
ToR to Host
G0/3

## Slide 20: Voltron Host Control and Dataplane
Contiv-GoBGP agent – advertise label/pfxs to the network, receive label/pfx info from the network
Contiv – programs label switching forwarding entries on host dataplane (OVS, VPP, etc.)
Could stop here if low-scale, single tenant, and no traffic engineering requirements…
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
Dataplane
Host
BGP-LU
BGP-LU
BGP-LU
payload
IP
111004
200.1.1.4/32
BGP-Pfx-SID 111004
200.1.1.4
payload
IP
111004
payload
IP

## Slide 21: Voltron Control Plane Scale
DC Fabric: small table sizes (lowest common denominator ~64k)
Host advertises prefix/label data to ToR – non-SRGB data
ToR does not advertise Host data to fabric
All prefix/label data sent to OpenBMP
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
Dataplane
Host
Fabric Domain BGP-LU
Host Domain BGP-LU
Host Domain BGP-LU
Fabric Topology, Label, Prefix Data
Host Topology, Label, Prefix Data
BMP Feeds

## Slide 22: Voltron Control Plane Scale
Fabric only knows SRGB data (ToRs, Leafs, Spines)
ToRs know locally attached Host prefix/label data
Connectivity Service creates |ToR-SRGB|Host-EPE|Prefix| tuple, and provides data to Contiv Agent
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
Dataplane
Host
200.1.1.4/32
Gi0/0/0/27,
EPE-SID 24027
200.1.1.4
Overlay Service
Msg Bus
Gi0/0/0/27
Contiv
Tuple:
100200,
24027,
200.1.1.4/32

## Slide 23: Voltron Dataplane Scale
Contiv Constructs SR label stack, programs forwarding entries on OVS/VPP
SR dataplane executes packet delivery (including ECMP)
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
Dataplane
Host
payload
IP
100200
200.1.1.4
payload
IP
24027
payload
IP
100200
24027
payload
IP
24027
Gi0/0/0/27
Contiv

## Slide 24: Voltron Multi-Tenancy
Very similar to MPLS-VPN
VPNv4 / VPNv6 between ToR and Host GoBGP
VPN Service Tuple expands to include VPN-SID: |ToR-SRGB|Host-EPE|VPN|Prefix|
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
23
Dataplane
Host
200.1.1.4/32
Gi0/0/0/27,
EPE-SID 24027
VPN-SID 99999
200.1.1.4
Overlay Service
Msg Bus
Gi0/0/0/27
Contiv
Tuple:
100200,
24027,
99999,
200.1.1.4/32
App
99

## Slide 25: Voltron Dataplane Scale
Contiv Constructs SR label stack, programs forwarding entries on OVS/VPP
SR dataplane executes packet delivery (including ECMP)
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
payload
IP
100200
24027
Gi0/0/0/27
Contiv
99999
App
23
Dataplane
Host
200.1.1.4
App
99
payload
IP
100200
24027
99999
payload
IP
24027
99999
payload
IP
99999

## Slide 26: Voltron Traffic Engineering (Path Selection)
Use BMP to export path attributes (ext-comms) from the network
Secure Path is reflected in Service Tuple label stack: |S2|ToR-SRGB|Host-EPE|VPN|Prefix|
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
App
23
Dataplane
Host
200.1.1.4
Secure Service
Msg Bus
Gi0/0/0/27
Contiv
Tuple:
100002
100200,
24027,
99999,
200.1.1.4/32
App
99
Secure Path ext-comm 0:2

## Slide 27: Voltron Traffic Engineering (Path Selection)
Contiv Constructs SR label stack, programs forwarding entries on OVS/VPP
SR dataplane executes packet delivery (including ECMP)
App
Dataplane
Host
S0
L4
L5
ToR100
L32
L33
S1
S2
S3
L6
L7
L34
L35
ToR
200
payload
IP
100200
24027
Gi0/0/0/27
Contiv
99999
App
23
Dataplane
Host
200.1.1.4
App
99
payload
IP
100200
24027
99999
payload
IP
24027
99999
payload
IP
99999
100002

## Slide 28: Voltron EPE Traffic Engineering (Peer Selection)
Probe Collector feeds peering data into Voltron Service
Contiv Constructs SR label stack, programs forwarding entries on OVS/VPP
SR dataplane executes packet delivery: DC exit, Egress Router selection, External Peer selection
App
Dataplane
Host
Contiv
Peer 1
SID 24001
DC1
DCI
A
DCI
B
App
Dataplane
Host
Contiv
DC2
DCI
A
DCI
B
User
User
User
User
Peer 2
SID 24002
Peer 3
SID 24003
WAN
Peering
A
Peering
B
Peering
C
Probe Collector
Probe
Probe
Probe
Voltron API GW

## Slide 29: Voltron EPE Traffic Engineering (Latency Peer Selection)
Probes measure latency through various peers
Collector injects data into Voltron DB; queryable through API GW
Endpoints ask for lowest latency path to users
App
Dataplane
Host
Contiv
Peer 1
SID 24001
DC1
DCI
A
DCI
B
App
Dataplane
Host
Contiv
DC2
DCI
A
DCI
B
User
User
User
User
Peer 2
SID 24002
Peer 3
SID 24003
WAN
Peering
A
Peering
B
Peering
C
Probe Collector
Probe
Probe
Probe
Voltron API GW

## Slide 30: Voltron EPE Traffic Engineering ($$ Peer Selection)
Admin injects peering cost data into Voltron Service
Endpoints ask for cheapest peering connection
App
Dataplane
Host
Contiv
Peer 1
SID 24001
DC1
DCI
A
DCI
B
App
Dataplane
Host
Contiv
DC2
DCI
A
DCI
B
User
User
User
User
Peer 2
SID 24002
Peer 3
SID 24003
WAN
Peering
A
Peering
B
Peering
C
Cost Collector
Probe
Probe
Probe
Voltron API GW
Admin System

## Slide 31: Voltron EPE Traffic Engineering (BW Peer Selection)
Collector injects link utilization data into Voltron DB; queryable through API GW
Endpoints ask for least utilized peering connection
App
Dataplane
Host
Contiv
Peer 1
SID 24001
DC1
DCI
A
DCI
B
App
Dataplane
Host
Contiv
DC2
DCI
A
DCI
B
User
User
User
User
Peer 2
SID 24002
Peer 3
SID 24003
WAN
Peering
A
Peering
B
Peering
C
BW Collector
Probe
Probe
Probe
Voltron API GW

## Slide 32: Voltron EPE Traffic Engineering (Peer Selection)
Contiv Constructs SR label stack, programs forwarding entries on OVS/VPP
SR dataplane executes packet delivery: DC exit, Egress Router selection, External Peer selection
App
Dataplane
Host
Contiv
Peer 1
SID 24001
DC1
DCI
A
DCI
B
App
Dataplane
Host
Contiv
DC2
DCI
A
DCI
B
User
User
User
User
Peer 2
SID 24002
Peer 3
SID 24003
WAN
Peering
A
Peering
B
Peering
C
Probe
Probe
Probe
payload
IP
DCI
Peering
EPE Peer
payload
IP
Peering
EPE Peer
payload
IP
EPE Peer
payload
IP
Voltron API GW

## Slide 33
Notes: Thank you for watching this video.